## Slide 1: Q1. CRC with G(x) = x³ + x + 1, data = 1011, received = 1011010. Error detected?
UNIT 2 · QUESTION 1 OF 5
Error Detection: CRC
A
No error
B
Error detected
C
CRC remainder = 0
D
Cannot determine
Given & Concept
Generator G(x) = x³ + x + 1 → 1011 (degree 3 → 3 CRC bits)
Data: 1011 · Received: 1011010
Remainder = Received ÷ G (mod-2)
Remainder 0 → accepted. Remainder ≠ 0 → error.
Solution
1
Valid codeword: 1011 + 000 → 1011000 (÷ 1011 gives remainder 0).
2
Divide received 1011010 by 1011 using XOR.
3
1011 ⊕ 1011 = 0000, leaving bits 010 → remainder = 010
4
010 ≠ 000 → the last bit was corrupted.
B
Error detected: remainder 010 is not zero.
EXAM TIP
Remainder 0 = clean. Anything else = error.

## Slide 2: Q2. Checksum of four 8-bit words 10011001, 11110000, 10101010, 00011111?
UNIT 2 · QUESTION 2 OF 5
Error Detection: Checksum
A
01001101
B
01100101
C
10011101
D
11100001
Given & Concept
10011001
11110000
10101010
00011111
Checksum = ~(sum with wraparound)
Add the words. If a carry comes out, add it back to the 8-bit sum. Then flip every bit.
Check: sum + checksum = 11111111.
Solution
1
10011001 + 11110000 = 1 10001001
Wrap carry: 10001001 + 1 = 10001010
2
10001010 + 10101010 = 1 00110100
Wrap carry: 00110100 + 1 = 00110101
3
00110101 + 00011111 = 01010100 (sum = 84)
4
Flip every 0 and 1 of 01010100 → 10101011
10101011
Computed checksum. No option A–D matches; the key's B (01100101) does not follow from the sum.
EXAM TIP
Add → Wrap the carry → Flip all bits.
Notes: Say in class: First, we add all four 8-bit binary numbers. If an extra carry comes out, we add it back to the 8-bit sum. After adding all the numbers, we take the 1's complement by changing every zero to one and every one to zero. Therefore, the checksum is 10101011. Shortcut: Add, wrap the carry around, flip all bits.

## Slide 3: Q3. Dataword length 11 bits; Hamming parity bits needed?
UNIT 2 · QUESTION 3 OF 5
Error Correction: Hamming Code
A
3
B
4
C
5
D
6
Given & Concept
Dataword length: m = 11
2^r ≥ m + r + 1
r = number of parity bits. The r bits must identify any of the m + r bit positions, or "no error".
Solution
1
r = 3: 2³ = 8 vs 11 + 3 + 1 = 15 → 8 ≥ 15 ✗
2
r = 4: 2⁴ = 16 vs 11 + 4 + 1 = 16 → 16 ≥ 16 ✓
3
r = 4 is the smallest value that works, so r = 4.
B
4 parity bits: the smallest r with 2^r ≥ m + r + 1. (The source key lists C; 5 also satisfies it but is not the minimum.)
EXAM TIP
Remember Hamming (15, 11): 11 data + 4 parity.

## Slide 4: Q4. Minimum distance of Hamming (7, 4)?
UNIT 2 · QUESTION 4 OF 5
Error Correction: Minimum Distance
A
2
B
3
C
4
D
5
Given & Concept
(n, k) = (7, 4): 7 codeword bits, 4 data bits, 3 parity bits
Detect s errors: dmin ≥ s + 1
Correct t errors: dmin ≥ 2t + 1
Solution
1
Hamming code corrects 1 error: t = 1
2
dmin ≥ 2(1) + 1 = 3
3
It also detects 2 errors: s = 2 → dmin ≥ 3
4
Hamming codes are designed with dmin = 3.
B
dmin = 3: corrects 1 error, detects 2.
EXAM TIP
Every Hamming code has dmin = 3.

## Slide 5: Q5. Probability single-bit error undetected by parity check?
UNIT 2 · QUESTION 5 OF 5
Error Detection: Parity Check
A
0
B
0.5
C
1
D
Depends on data
Given & Concept
A parity bit makes the number of 1s even (or odd).
Parity detects every odd-bit error
Only even numbers of flipped bits (2, 4, …) can slip through.
Solution
1
Sender sends a word with even parity.
2
One bit flips (0 → 1 or 1 → 0).
3
The count of 1s changes by exactly ±1, so it becomes odd.
4
The receiver sees odd parity: always detected, so P(undetected) = 0.
A
0: a single-bit error is always detected, whatever the data.
EXAM TIP
Odd errors caught; even errors missed.