## Slide 1
Q1
A 100 Mbps link has 50 ms one-way delay. What is the bandwidth–delay product?
OPTIONS
A
0.5 Mb
B
5 Mb
C
50 Mb
D
500 Mb
STEP-BY-STEP EXPLANATION
Formula: BDP = Bandwidth × One-way delay
Convert units: 100 Mbps = 100 × 10⁶ bits/s; 50 ms = 0.05 s
BDP = 100 × 10⁶ × 0.05 = 5 × 10⁶ bits
5 × 10⁶ bits = 5 Mb, which matches option B
FINAL ANSWER
B. 5 Mb

## Slide 2
Q2
A 1.5 Mbps link has RTT = 100 ms and a full window of 10 packets of 1 KB each. What is the throughput?
OPTIONS
A
120 kbps
B
500 kbps
C
800 kbps
D
1.2 Mbps
STEP-BY-STEP EXPLANATION
Formula: Rate = min(Window ÷ RTT, Link rate)
Window = 10 × 1 KB = 10 KB = 80 kb; RTT = 0.1 s
Window ÷ RTT = 80 kb ÷ 0.1 s = 800 kbps
Link rate = 1500 kbps, so the window is the bottleneck: min(800, 1500) = 800 kbps
FINAL ANSWER
C. 800 kbps

## Slide 3
Q3
A 5 Gbps channel has a propagation delay of 20 ms. What is the maximum number of bits in transit?
OPTIONS
A
100 Mb
B
10 Mb
C
1 Gb
D
50 Mb
STEP-BY-STEP EXPLANATION
Formula: Bits in transit = BDP = Bandwidth × Delay
Convert units: 5 Gbps = 5 × 10⁹ bits/s; 20 ms = 0.02 s
BDP = 5 × 10⁹ × 0.02 = 1 × 10⁸ bits
1 × 10⁸ bits = 100 Mb, which matches option A
FINAL ANSWER
A. 100 Mb

## Slide 4
Q4
A satellite link has 270 ms one-way delay and 10 Mbps bandwidth. What is the BDP?
OPTIONS
A
2.7 Mb
B
5.4 Mb
C
8.1 Mb
D
10 Mb
STEP-BY-STEP EXPLANATION
Formula: BDP = Bandwidth × One-way delay
Same convention as Q1 and Q3
Convert units: 10 Mbps = 10 × 10⁶ bits/s; 270 ms = 0.27 s
BDP = 10 × 10⁶ × 0.27 = 2.7 × 10⁶ bits = 2.7 Mb
Note: with RTT (540 ms) it would be 5.4 Mb (option B)
FINAL ANSWER
A. 2.7 Mb

## Slide 5
Q5
For stop-and-wait ARQ, link 2 Mbps, RTT = 40 ms, frame = 1000 B. What is the efficiency?
OPTIONS
A
0.2
B
0.4
C
0.1
D
0.5
STEP-BY-STEP EXPLANATION
Formula: Efficiency = Tx ÷ (Tx + RTT)
Frame = 1000 B = 8000 bits = 8 kb
Tx = 8 kb ÷ 2 Mbps = 8000 ÷ (2 × 10⁶) = 4 ms
Efficiency = 4 ÷ (4 + 40) = 4 ÷ 44 ≈ 0.09
0.09 is closest to 0.1, which is option C
FINAL ANSWER
C. 0.1

## Slide 6
Q41
A channel has 2 MHz bandwidth and SNR = 10 dB. What is the capacity?
OPTIONS
A
6.6 Mbps
B
13.3 Mbps
C
20 Mbps
D
2 Mbps
STEP-BY-STEP EXPLANATION
Formula: C = B × log₂(1 + SNR)
B = 2 MHz = 2 × 10⁶ Hz; SNR = 10 dB → 10^(10/10) = 10
C = 2 × 10⁶ × log₂(11) ≈ 2 × 10⁶ × 3.46
C ≈ 6.9 Mbps, so the closest option is 6.6 Mbps (option A)
FINAL ANSWER
A. 6.6 Mbps